## Slide 1
A desire to complete our Team Vision from last semestral project
A brief on last project….
Project Selection
Notes: Let me just kick off with our project selection. – It stemmed from our last semester’s project.
The team reviewed last semestral project and all agreed that we should finish off our unfinished Team Vision
Allow me to briefly run through our last project.

## Slide 2: Project Title In the light of Covid-19, how might customers feel safer while shopping through Smart Technologies? Case Study at DECATHLON Store
Last Project
Notes: This was our project title. The project concept then was conceived to coincide with the Health Ministry task force on safe management measures.
We used Decathlon Store as our case study.

## Slide 3
Limited Sensors
Net Customers Count
AWS
EPS32 +
Ultrasonic Sensor
Team Vision
Book queue/SMS notification
Live update on web
Notes: In the safe management measures, one of the advisories is permit mega store like Decathlon to hold max customer capacity based on Gross Floor Area or GFA.
Our team undertook the vision to implement 3 applications satisfy smart technologies:
- sensors that track the number of customer in store
- upload, publish and display the info on the cloud
- provision a mobile app for customer to book and join queue instead of queuing outside store.
3. At end of project implementation, it was obvious here that we could managed 2 applications.

## Slide 4
This semester…
To accomplish our vision by working on the remaining mobile app, and along with enhanced sensors to automate the SMM process
Notes: But we save the best for last. Now that we are better equipped with mobile app programming knowledge, our team is determined to accomplish our unfinished vision.
And along with the knowledge learnt from the Sensor and Communication Technologies module, to further implement a suite of collective sensors to implement an automated safe management measures process.

## Slide 5
Enhanced Sensors
Automated for control entry access
Process customer count and upload to cloud
Firebase
Operative Concept
Crowd information
Book queue
SMS notification
Provision of Webpage on number of customers at various store locations
Notes: This is the concept of operation.
The sensors are to provide automated entry access as well as to process the net customer count, upload and update the cloud.
The cloud provides a webpage on the number of customers at various store locations. It also store data for mobile app to draw the relevant info.
The mobile app provides information on the number of customers at various store locations and allow customer to book queue and be informed on the queue status via sms notification.

## Slide 6
Sense and Sensibility
Clearly articulate the problem
Develop a deep understanding of the challenge
Empathy
Brainstorm solutions, select and develop solution
Ideation
Enhance the prototype towards automation
Prototype*
Design Thinking
Notes: The Design Thinking tool help to validate the continuation of this project.
We reviewed the chain of processes, by and large we derived with the same outcome as the last project.

## Slide 7
Sense and Sensibility
The problem statement involves an end user, problem to be tackled and a probable solution.
Our project statement defined “how might customers feel safer while shopping through Smart Technologies? ”
2) Empathy - POEMS
Design Thinking
P - People
Impatient Customers
Customer with kids
Elderly customers
Absence of signage for customer
Confusion among staff
Notes: The next few slides are further details of our review

## Slide 8
O - Object:
  Lack of queuing pole guide
            E - Environment:
              Aircon too cold, discomfort
              Lack of 1-metre markers
  M - Message/Media:
    Unclear instruction
    Lack of customer count in store
    Lack of waiting time info
        S - Services:
          Ease customer frustration
          Option to other outlets
Design Thinking

## Slide 9
Insights/Observation
From POEMS we gain the insight/observation as follows:
Design Thinking
Lack of signage / info / est. waiting time
Staff under pressure from customers
Oversight of exceeding occupancy limit

## Slide 10
c) Persona
Design Thinking

## Slide 11
3) Ideation
a) Brainstorming
After 15 mins of brainstorming below are the ideas generated:
Design Thinking

## Slide 12
b) Matrix Analysis
Using matrix analysis we narrowed down to three ideas that are both desirable and feasible:
  Using sensors at all the entrances and exits to gather the number of people going in and out of the store, and upload to cloud
  Sensor system to be automated, minimizing staff manning.
  Mobile app to let customers determine which less crowded stores to shop based on the number of people in the queue (if any)
  Using mobile app to let the customer book queue. This minimize large queue outside the store.
  Data with current customers count from each of the 5 physical stores could be updated live to the cloud.
Design Thinking

## Slide 13: Project Title Digital Solutions for An AUTOMATED Crowd Control Management @Decathlon
Notes: 1. With the Design Thinking tool, we not only arrived with the same goal of achieving crowd control management, and one with a fully digital and automated solution.

## Slide 14: Decathlon Crowd Management System
Arduino Uno
LoRa/Wifi/Bluetooth
LoRa/Wifi/Bluetooth
Firebase Cloud
Mobile Apps for Info Retrieval/SM Notification
LCD
Counter
Ultrasonic Ranger
Buzzer
Warning
Servo
LoRa for update of exit count
Obstacle Avoidance IR
Wifi for update of net count
Entry Sensor
Exit Sensor
Entrance Arduino
Process net customer count from both entrance and exit and upload to cloud SQL.
Update and display counter on the no. of customers.
Control barrier for customer entry.
Exit Ardunio
Count customer exit and update Entrance Arduino for process.
Decathlon Mobile Apps
One module dedicated to SMM application on top of browsing catalogue.
Check crowd management status and book queue if needed.
Receive SMS notification.
Distance between entrance and exit points more than 100 m apart and blockage of AP
Obstacle Avoidance IR
LED
Warning

## Slide 15: Decathlon Crowd Management System
Arduino Uno
Firebase Cloud
LoRa for update of exit count
Wifi for update of net count
Entry Sensor
Exit Sensor
Entrance Arduino
Process net customer count from both entrance and exit and upload to cloud SQL.
Update and display counter on the no. of customers.
Control barrier for customer entry.
Exit Ardunio
Count customer exit and update Entrance Arduino for process.
Decathlon Mobile Apps
One module dedicated to SMM application on top of browsing catalogue.
Check crowd management status and book queue if needed.
Receive SMS notification.
Distance between entrance and exit points more than 100 m apart and blockage of AP

## Slide 16: Schematic Set Up

## Slide 17: Operation Flow Chart
UNO
If Count <=50
Check & display customer Count
LoRa
Update net count to Cloud
via Wi-fi
See You Again (OLED)
Detect customer exit (IR)
Customer exits?
ESP32 Exit
Yes
No
Open barrier (Servo)
Barrier Opening Alarm (LED & Buzzer
Detect customer entry (IR)
Update Customer Count
No
Yes
LoRa (net count)
Yes
No
Pass temp?
Presence of Cust?
Entry not permitted
Next customer takes temp
Customer to wait or take queue no
Display capacity exceeded
Barrier Open()
Close barrier()
Barrier closing Alarm (LED & Buzzer
No
ESP32 Entry

## Slide 18: Program Flow (UNO)
Net customer < max capacity
Display net customer in Store (LCD)
Close barrier at start of program
Display “Next customer, please take temp” (LCD)
Ultrasonic sense customer within “1m”
Temp sensor takes temp (DHT11)
If temp < 32.0
Display “Your temp is xxC” (LCD)
Display “Entry permitted, Pls enter store” (LCD)
Display “Caution “Barrier opening” (LCD)
Warning Alarm (led & buzzer)
Open barrier (servo)
Display “Please enter now” (LCD)
Display “Caution!!! Barrier closing” (LCD)
Display “Barrier closing” (LCD)
Warning Alarm (led & buzzer)
Else temp > 32.0
Display “Temp is xxC” (LCD)
Display “Temp is HIGH!” (LCD)
Display “Entry not “permitted” (LCD)
Net customer > max capacity
Display “Crowd capacity exceeded” (LCD)
Ensure barrier is closed
Ensure barrier remains closed
UNO@Entry

## Slide 19: Program Flow (Entry & Exit)
Check incoming packet from ESP32@Exit (via LoRa)
Update net customer count to UNO@entry (via Soft serial)
Check for customer entry (via IR sensor)
Update Firebase cloud via Wifi
Display “Welcome!” (OLED)
Update ESP32@Entry (via LoRa)
Check for customer entry (via IR sensor)
Display “See you soon!” (OLED)
Check for customer exit (via IR sensor)
ESP32@ Exit
ESP32 @Entry

## Slide 20
Android Mobile Application will incorporate 3 Technical criterias :
- WebView via web
- SMS or Email, Alarm or Notification via mobile phone
- Cloud Service hosted by ThinkSpeak (tbc)
Mobile App Development
Notes: To satisfy the 3 mobile app technical contents, our project will leverage on
  - WebView, SMS notification & Cloud Service.

## Slide 21: Project Group Members: 1. Ng Chye Soon (Adm No.P7014423) 2. Ng Wai Cheong (Adm No: P7319713) 3. Choong Foo Chung (Adm No: P7825599) 4. Karen Loke Chia Wai (Adm No : P7075382)
School of Electrical and Electronic Engineering (EEE)
Specialist Diploma in Digital Technologies for Smart City
Notes: Last of all, these are my project team members!

## Slide 22: ThE END Thank-you